MV “BLIDOE”

| MAIN PARTICULARS: Flag : Cyprus Port of registry : Limassol Built: : April, 2008, Bodewes Type : Multipurpose Class : DNV GL 100 A5 E2 G MC E2 AUT Ice Class : 1B Finnish-Swedish Ice Class IMO Nr. : 9393840 EORI Nr. : DE422138249423025 P&I : Skuld H+M value : EUR 5 Mio GENERAL DIMENSIONS: GT/NT : 4.102 / 1.851 DWT summer sw : 5.490 Draft fully laden sw : 5,25 m LOA : 106,86 m LPP : 100,62 m Beam : 15,20 m Depth moulded : 8,70 m Ballast airdraft : 26,00 m Distance wl/hc : abt 6,25 m ballast, abt 4,68 m laden DECK STRENGTH: Tanktop strength : 15,00 mts / sqm Hatchcover strength : 1,75 mts / sqm CONTAINER DATA: Container intake : 279 TEU total 168 TEU (hold) + 111 TEU (deck) : 111 FEU total 60 FEU (hold) + 51 FEU (deck) Intake is always subject vessel’s stability, trim, permissible weight and is subject to regulations of visibility. | HOLD PARTICULARS: Grain capacity : 295.396 cbf (8364 cbm) Holds/hatches : 2/2; boxshaped narrowing fore/aft – L 8,20 m to B = 8,00 m Hold No 1 / 2 (grain) : 144.674 cbf /150.722 cbf (4.096,71/4267,98 cbm) Hold 1 (LxBxH) : 37,50 m x 12,65 m x 8,99 m (29,25 m length without narrowings) Hold 2 (LxBxH) : 37,50 m x 12,65 m x 8,99 m (35,75 m length without narrowings) Hatch 1+ 2 : 37,50 m x 12,65 m Hatch covers : pontoon, 12 pcs (operated by gantry crane) Moveable bulkheads : 2 bulkheads Hold ventilation : 12.500 cbm/h airchanges in hold MACHINERY: Main engine : Caterpillar MAK 6 M 2030 KW Diesel generators : 280kw 140/140 kw each Shaft generator : 350 kw Bow thruster : 300 kw Propeller : CPP Speed/consumption : abt 11 kn on abt 8,5 ts RME 180/MGO p.d. Port consumption per day : abt 0,50 mt GO per day Heavy fuel oil IFO180, RMG180 – ISO8217-2010 MGO – ISO8217:2010E – Category ISO/F – DMA s.w. max 0,89 No GO at sea provided shaft generator connected except if hold ventilation is used, and in case of emergency and/or maneuvering in/out of ports and when navigation is shallow, narrow or other constraint waters. TANK CAPACITIES: HFO : 215,557 cbm MGO : 70,192 cbm Fresh water : 36,664 cbm Ballast water : abt 2879,067 cbm |
| --- | --- |